## Slide 1
IoT-Based Smart Rental Locker System
Prototype Design: Integrated Hardware, Web Backend, & UPI Verification Flow

## Slide 2
Project Overview & Core Features
• State-Driven Architecture: Avoids recursive loops and display flickering.
• HTTP-Based Polling Loop: The ESP32 polls the server status endpoint every 3 seconds.
• Out-of-Band Physical OTP: Dynamic 6-digit retrieval code is shown on the locker screen.
• Local SQLite Ledger: SQLite tracks bookings, locker states, and payments dynamically.
• verification Page: Web app verifies payment reference number (UTR) to activate storage locks.

## Slide 3
1. Complete System Block Diagram
System Architecture & Interactions:
The prototype coordinates physical hardware locks with web databases and UPI payment confirmation via local network protocols.
1. The ESP32 acts as the physical client, continuously polling the Flask backend via secure Wi-Fi HTTP requests to check current states.
2. The Flask Backend manages relational logic and booking timers, reading and writing to an SQLite transaction database.
3. Users interact via a mobile web portal to book lockers, view instructions, and submit transaction UTR codes to unlock doors.
4. This decoupled system eliminates cellular SMS gateway dependencies by rendering the retrieval OTP directly on the locker's physical TFT screen.

## Slide 4
2. Full Circuit Design & Connections
Hardware Connections & Interfaces:
The circuit integrates an ESP32 board, a 2.4" SPI TFT LCD screen, and an SG90 analog servo motor.
• ESP32 NodeMCU LX6: Operates at 240 MHz, handles SPI display drawing and PWM servo control.
• SPI TFT Display: Pin connections CS (GPIO 15), RESET (GPIO 4), D/C (GPIO 2), MOSI (GPIO 23), and SCK (GPIO 18).
• SG90 Servo Control: High-torque servo powered from Vin (5V) to prevent brown-out resets, driven by a 50Hz PWM signal from GPIO 26.
• Common Ground: All components share a common ground (GND) to maintain electrical logic levels.

## Slide 5
Hardware Datasheet Specifications
• ESP32 Microcontroller: 3.3V logic level (maximum current output per GPIO is 12mA). Powers down USB-to-UART bridge when idle.
• ILI9341 2.4" TFT: Screen requires ~3.3V power, 320x240 pixels (RGB), 16-bit color. Draw logic driven by hardware SPI lines.
• SG90 Micro Servo: Stall torque 1.8 kg-cm. Operating voltage 4.8V - 6V. Requires Vin connection since 3.3V rail lacks sufficient surge current.
• Backlight Power: TFT backlighting LED requires 20mA. Driven from 3.3V rail through a 100-ohm current-limiting resistor.
• Logic Protection: Connecting 5V components directly to ESP32 inputs requires level shifters or resistor divider networks to protect GPIOs.

## Slide 6
3. Software State Machine Flowchart
State Transition Matrix:
The firmware functions as a state machine governed by the backend DB booking state:
1. STATE_AVAILABLE: Displays website QR code on screen. Servo is 0° (locked).
2. STATE_PENDING_PAYMENT: Displays payment UPI QR code on screen.
3. STATE_WAITING_FOR_CLOSE: Payment verified, servo unlocks to 90° (door open).
4. STATE_ACTIVE_RENTAL: Locker door locked, TFT screen renders RTC rental timer.
5. STATE_OTP_GENERATED: Renders large centered white card containing 6-digit OTP.
6. STATE_RETRIEVAL_APPROVED: OTP verified, servo unlocks to 90° for item retrieval.

## Slide 7
Presentation Q&A & Key Benefits
Q: Why use a TFT Screen to display the retrieval OTP?
A: SMS gateways charge recurring fees and have delivery latency. TFT display OTP acts as a zero-cost physical proof of presence factor.
Q: How is the locker servo secured during database timeouts or crashes?
A: Servo requires continuous PWM signals to move. Without power or on crash, it holds position. Status is restored upon ESP32 reboot.
Q: How does automatic payment detection work in the prototype?
A: Users submit their transaction UTR on the web portal. The backend verifies the UTR formatting and sets status to paid.